RFP 196 OSGi Connect
Draft
Pages
Abstract
Discusses the needs for a specification that would make code and services from outside of an OSGi framework available to OSGi and vice versa.
# Document Information
## Table of Contents

## Terminology and Document Conventions
The key words "MUST", "MUST NOT", "REQUIRED", "SHALL", "SHALL NOT", "SHOULD", "SHOULD NOT", "RECOMMENDED", "NOT RECOMMENDED", "MAY" and "OPTIONAL" in this document are to be interpreted as described in 6.1.
Source code is shown in this typeface.
## Revision History
The last named individual in this history is currently responsible for this document.

Revision	Date	Comments
Initial	2019-05-29	Carsten Ziegeler, Initial draft based on RFP-143 and F2F discussion in Chicago

# Introduction
This RFP discusses the needs for an OSGi Framework to use modules which are not controlled by the framework. This allows to connect the OSGi Framework with code and services from the outside world like jars on a classpath.
Parts of this work were first explored in RFP-143 OSGiConnect. Although RFP-143 got accepted it never made it into an RFC. This RFP is taking the basic ideas and generalizing it to allow for an adjusted set of use cases.
# Application Domain
The OSGi framework consists of a number of layers where the module layer is by far the largest and most complex. This layer has shown to be very useful for large and complex applications that require side by side versioning and encapsulation of their classes.
The OSGi module layer takes care of the class loading for each bundle and isolates bundles in their own class loader, minimizing global space. The consequence of the module layer being responsible for class loading, prevents or at least makes it very difficult to use classes or services that are already present on the class path and which class space is managed outside of OSGi.
At the same time, functionality running outside of OSGi is not able to benefit from the rich service model of OSGi in a standardized way.
## Terminology + Abbreviations
OSGi Connect – Working name given to this effort.
Connect Bundle – A connect bundle is a module provided from outside of the OSGi framework and represented within the OSGi framework as a bundle. A connect bundle is usually already fully wired and can’t be changed at runtime. Apart from that it can function as a proper bundle but might have some limitations with respect to class loading and isolation which need to be defined during the specification process.
# Problem Description
There is a need for a solution that allows Java developers to connect the OSGi service and module model to code and services running outside of the OSGi framework. This opens up OSGi to “normal” Java applications and allows to use OSGi functionality for dedicated use cases. At the same time, OSGi gets access to the outer world and is not losing any of its functionality and benefits.
# Use Cases
## bnd in Ant and Maven
bnd, the OSGi tool to make manifests, is an eclipse plugin, an ant task, a bundle, and a command line utility. Because it has to run inside Ant and Maven it cannot rely on the presence of an OSGi framework. For this reason, it sadly implements a plugin model based on class loaders. If a (light weight) OSGi was available that provided the OSGi service registry to outside code to allow to isolate bnd plugins then bnd could carry this OSGi Connect in its Ant task and Maven plugin.
## WARs
The Java EE is a highly popular format for deploying web applications. The different servlet bridges have made it possible to use OSGi inside the WARs but especially in Java EE based applications the class loading issues are prevalent. An OSGi Connect could be triggered when a servlet is loaded and thereby activating all “bundles” and let them collaborate through the service registry.
## Application Frameworks
Numerous application frameworks exist to provide convenient access to various services ranging from parsing, logging, and security to web access and persistence. The popularity or usefulness of a given framework could lead it to be adopted and even relied upon by an application. Unfortunately, some frameworks have intrinsic dependencies and built-in assumptions about the classloader environment. In some cases these frameworks will not function correctly in OSGi. OSGi Connect is one way to enable applications to use some of the benefits of OSGi services and modules, but still be able to make use of existing frameworks.
## Build a hybrid OSGi-JPMS application
A Java application may have some of it’s functionality implemented as bundles and another part implemented as modules. It should be possible to use JPMS modules within an OSGi framework.
## Applications with a flat classpath
In some scenarios its common to package a Java application as a single jar with all the jars embedded. Usually a custom classloader is used to add all embedded jars to the classpath and then the application is launched. In these scenarios all jars/modules are already on the classpath and a contained OSGi framework does not need to provide module isolation and can directly use the jars as bundles, still providing most of the OSGi functionality.
# Requirements
## Basic
- BA0010 – It must be possible to install Connect Bundles. A connect bundle is an entity that is already on the class path of the framework.
- BA0020 – It must be possible to add, update and remove services to/from the service registry from the outside of the framework.
- BA0030 – It must be possible to use OSGi services implementing an API provided by a Connect Bundle outside of the OSGi framework.
## Connect Bundle
- CB0010 – It must be possible to provide the class loader for a connect bundle.
- CB0020 – It must be possible to provide the wiring information of a connect bundle.
- CB0030 – It must be possible to provide the manifest header of a connect bundle.
- CB0040 – It must be possible to provide the resources/entries of a connect bundle.
- CB0050 – Connect bundles must be treated and behave like any other bundle except for a limited set of functionality that is not supported in this case.
# Document Support
## References
1. Bradner, S., Key words for use in RFCs to Indicate Requirement Levels, RFC2119, March 1997.
2. Software Requirements & Specifications. Michael Jackson. ISBN 0-201-87712-0

## Author’s Address

Name	Carsten Ziegeler
Company	Adobe
Address
Voice
e-mail	cziegele@adobe.com

Name	Karl Pauls
Company	Adobe
Address
Voice
e-mail	kpauls@adobe.com

## End of Document