Security Improvement for Configuration Admin Service
Draft
Pages

Abstract
Though OSGi is integrated with Java2 Security Model, some important resources are not protected by permissions. There is a permission with too coarse-grained scope to use in some application domains. This RFP clarifies the resources to be protected and a permission to be finer-grained. The resources are related to Configuration Admin Service.
# Document Information
## Table of Contents

## Terminology and Document Conventions
The key words "MUST", "MUST NOT", "REQUIRED", "SHALL", "SHALL NOT", "SHOULD", "SHOULD NOT", "RECOMMENDED", "NOT RECOMMENDED", "MAY" and "OPTIONAL" in this document are to be interpreted as described in 6.1.
Source code is shown in this typeface.
## Revision History
The last named individual in this history is currently responsible for this document.

Revision	Date	Comments
Initial	June 5 2008	First Draft / Hiroyuki Maeomichi, NTT, maeomichi.hiroyuki@lab.ntt.co.jp / Ikuo Yamasaki, NTT, yamasaki.ikuo@lab.ntt.co.jp
2nd	Sep 4 2008	The descriptions related with Http Service are removed from the document due to the result of discussion on conference call with BJ. In addition, the title is changed. / Ikuo Yamasaki, NTT, yamasaki.ikuo@lab.ntt.co.jp
3nd	Sep 24, 2008	The last paragraph of Sec 3.1 that had limited the bundle identifier only to location is removed due to the result of discussion on F2F meeting in NJ. Filter can include not only location but also bundle id, symbolic name, and signers. / Ikuo Yamasaki, NTT, yamasaki.ikuo@lab.ntt.co.jp

# Introduction
Though OSGi is integrated with Java2 Security Model, some important resources are not protected by permissions. There is a permission with too coarse-grained scope to use in some application domains. This RFP clarifies the resources to be protected and a permission to be finer-grained. The resources are related to Configuration Admin Service.
# Application Domain
R4.1 spec defines Configuration Admin Service specifications, which provides unified way for privileged bundles to set configurations for other bundles and for a bundle to use those configuration. The privileged bundles are bundles given ConfigurationAdminPermission.
## Terminology + Abbreviations

# Problem Description
ConfigurationPermission introduced in R4.1 doesn't realize fine-grained control for access to Configuration objects. Current granularity of the permission allows independent bundles to interfere each others through changing configuration.
## Configuration objects bound to locations
In ConfigurationAdmin Service Specification 1.2, a bundle granted ConfigurationPermission can get Configuration objects bound to any bundles' locations and a bundle not granted ConfigurationPermission can get no Configuration objects except the ones bound to own bundle location. In other words, the following scenario is impossible to realize: bundle 1 is allowed to get Configuration objects of bundle1 and bundle 2, but not to get ones of bundle 3. In order to realize this, ConfigurationPermission must be changed to support a filter expression for its name as similarly as change of AdminPermission in Core Specification 1.3 (release 4.0).
# Use Cases
## Use case for configuration objects bound to locations

Assume that the multiple service provider model[6][7] case: both bundle A and B belong to segment 1 provided by Service Provider 1 and both bundle C and D belong to segment 2 provided by Service Provider 2 where all of them are ACTIVE on the same OSGi framework. On the one hand, bundle A desires to update not only Configuration objects bound to bundle A but also Configuration objects bound to bundle B. On the other hand, Service Provider 2 doesn't want for any bundles provided by other Service Providers to update Configuration objects of bundle C and D( Fig. 1). The management agent of the platform needs to restrict those access control beyond segments.

Fig 1:Use case for fine-grained access control to configuration objects
# Requirements

ConfigurationPermission should support not only wildcard but also filter expression regarding bundle identifiers in its name argument for fine-grained access control to Configuration objects.
# Document Support
## References
1. Bradner, S., Key words for use in RFCs to Indicate Requirement Levels, RFC2119, March 1997.
2. Software Requirements & Specifications. Michael Jackson. ISBN 0-201-87712-0
3. http://java.sun.com/products/servlet/
4. PERSISTENT CLIENT STATE HTTP COOKIES, http://wp.netscape.com/newsref/std/cookie_spec.html
5. Kristol, D., HTTP State Management Mechanism, RFC 2109, February 1997

Koya, M., et al., OSGi Alliance, RFC-131: Multiple Service Provider Separation

Hiroyuki, M. et al., OSGi Alliance, RFC-135: Referene Architecture for Multiple Service Providers Environment

## Author’s Address

Name	Hiroyuki Maeomichi
Company	NTT
Address	1-1 Hikarino-oka Yokosuka Kanagawa Japan
Voice	+81 468 59 3013
e-mail	maeomichi.hiroyuki@lab.ntt.co.jp

Name	Ikuo YAMASAKI
Company	NTT
Address	1-1 Hikarino-oka Yokosuka Kanagawa Japan
Voice	+81 468 59 8537
e-mail	yamasaki.ikuo@lab.ntt.co.jp

## End of Document